## Slide 1
Agenda point 2a)
Plans for handling of losses on HVDC cables in NWE day-ahead price coupling
IG Meeting
Copenhagen 19. September 2012

## Slide 2
NWE TSOs agreed basis
APCA Annex 5
  "The Algorithm shall ensure that it is possible to implement losses in the flow calculation for interconnectors within an ATC based area and for interconnectors between ATC based areas and flow based areas. Losses are not implemented between two bidding areas if no interconnector is explicitly defined. If any interconnector owner requires that losses shall be included in the optimisation on all or parts of his network, the PX is required to do so."
The methodology, which is included in the PCR Algorithm, will be used where losses are implemented on HVDC interconnectors

## Slide 3: Capacity provisions and loss procurement
Losses not included in the algorithm:
In D-1, TSOs assess and pre-order expected losses to ensure in real time the balance production and consumption
Losses are procured by the TSOs outside the allocation
Leads to imbalances on the ordered losses due to inaccuracies
Losses included in the algorithm:
The handling of losses is integrated with the allocation. The shipper procures/sells different energies on each side of the cable. Costs of losses are borne directly by the Market Participants
Market prices better reflect marginal cost of supply (i.e. Including losses incurred in the transaction).
Flow pattern, losses in neighbouring countries and prices will change.
Losses will cause minor price differences over a DC interconnector
Potential imbalance for loss volume due to ID trade
Potential impact on other timeframes
TSOs determine the available capacity by the same principles as today.
  Inclusion of losses will therefore not cause changes to the available capacity given to the market

## Slide 4
Loss modelling in PCR Algorithm
Possibilities by the algorithm Linear losses are allowed, i.e the losses is a fixed percentage of the flow
Deciding the loss factor
Necessary analysis will define the percentage
TSOs specify losses percentage based on actual losses for individual DC line(e.g. IFA ~2%, NorNed~4%)
Energy Balance
The sum of net positions plus losses is equal to zero
Price Properties
mcpto (1-loss) - mcpfrom = 0 when no congestion (no congestion rent),
mcpto (1-loss) - mcpfrom > 0 when line is congested
The price difference will be sufficient to cover the costs of losses when the cable is uncongested
1040 MW
1000 MW
F in=1040 MW
F out = F in- losses= 1000 MW
HVDC Losses ~ 4 %

## Slide 5: European or national decision to activate loss functionality
Regional/global analysis required before implementation:
  Welfare and SoS perspective for regions
  Effects of neighbouring networks and other timeframes if only implemented in DA
  Connection with inter TSO compensation mechanism
  Potential conflict with the provisions in Regulation 714/2009 which prohibits border tariffs and the use of congestion rents.
Global/regional issue
Local/bilateral issue
APCA annex 5 states clearly that it is a national issue (provided approval by local NRAs)
BritNed and IFA has already implemented losses. Baltic Cable has requested EMCC to implement it.
  Local TSO Rules are approved by the Local NRA, (but in cooperation with other NRAs).
Many other local decisions effect flows (and SoS) in neighboring networks