## Slide 1
NWE Day Ahead Price Coupling
Handling of losses
in the algorithm
IG MEETING 5. DECEMBER

## Slide 2: Background
The NWE Project presented how losses will be implemented in the algorithm at the IG meeting of September 19th in Copenhagen
NRAs agreed to post several questions to the TSOs to asses the consequences of implementing losses
The TSOs received a request including 10 questions from the NRAs on October 1st.
The NRAs have asked for answers by the following IG meeting, i.e. December 5th.
TSOs have responded that this would not be possible due to time constraints and lack of simulation tools. The response will be provided by first IG meeting in 2013 (assumed by end February)

## Slide 3: Losses modelling in PCR Algorithm
Possibility for the algorithm
Linear losses are allowed, i.e. the losses are a fixed percentage of the flow.
Deciding the loss factor
Based on a technical analysis the percentage is defined.
TSOs specify losses percentage based on actual losses for individual DC line (e.g. IFA ~2%, NorNed~4%)
Price Properties
mcpto (1-loss) - mcpfrom = 0 when no congestion (no congestion rent),
mcpto (1-loss) - mcpfrom > 0 when line is congested
The price difference will always be sufficient to cover the costs of losses when the cable is uncongested
Energy Balance
The sum of net positions plus losses is equal to zero
1040 MW
1000 MW
F exp=1040 MW
F imp = F exp- losses= 1000 MW
HVDC Losses ~ 4 %

## Slide 4: Impact assessment on losses
Following simulations have been agreed between TSO and PXs
Run #1 – No losses at all - The output is the reference result in terms of social welfare, prices and flow pattern
Run #2 – Harmonised Loss Factor (say 2%) on all existing DC cables (harmonized case) / No loss on AC interconnectors
Run #3 – Individual Loss Factor (2.34% IFA, 2.5% Kontek, 3.6% Skagerrak…) on all existing DC cables / No loss on AC interconnectors
Run #4 – Individual Loss Factor on some DC cables (BritNed, IFA and Baltic) / No loss on AC interconnectors
Run #5 – Harmonised Loss Factor in some DC cables (BritNed, IFA and Baltic) / No loss on AC interconnectors
  The outcome in terms of flow patterns might need additional simulations with the flow calculation prototype (3-step approach including pro-rata rule for UK) where there are flow indeterminacies
Indicators:
Overall social welfare and breakdown of welfare to individual countries for consumer and producer surplus. Congestion revenue per border. Results compared to reference case (Run 1, which excludes any losses)
Interconnector flows (commercial flows as calculated by the algorithm) compared to reference case
Market clearing prices compared to reference case

## Slide 5: Further work
The release #1 and #2 of Euphemia include the loss functionality. The flow calculation will not be included until release #3 which is final tested by end December.
The TSOs propose therefore that simulations are done based on release #3 of the algorithm and including of flow calculations.
Simulations can start early January if the test has been successful
The TSOs will hire an external consultant to write a report/answer the questions.
A more detailed plan for this work will be sent to the NRAs when it has been agreed among TSOs and PXs