## Slide 1: Discussion on Intraday Capacity Pricing
NWE ID project
2011-10-10

## Slide 2
The following slides are still work in progress. The presentation reflects the current status of discussions between NWE TSOs and an initial exchange of ideas with NWE PXs. There are some issues that still or after a second thought need to be clarified, eg. definition of scarcity, congestion rent in relation to additional capacity

## Slide 3: Content
Introduction
  Objective
  Terminology
  Ranking vs. Pricing
  Legal background
Ranking
  Allocation principles
  Implicit access (SOB)
  Summary
Pricing of Capacity
Appendix

## Slide 4
The objectives of this set of slide is to describe the areas where capacity has a value, and to list how this value should be reflected in the IDXB solution
Further the slides shall demonstrate that TSOs are making a clear distinction between Ranking (mechanism to meet an efficient allocation of capacity) and Pricing (mechanism to generate revenues when network congestion)
Ranking and Pricing of intraday capacity should be assessed against some main, non exhaustive criteria such as:
  Short term: allocate capacity efficiently in a market-based manner, ensuring that capacity is allocated to who is valuing the capacity the most
  Mid term: ensure consistency between the different timeframes such as day-ahead (notably in order to run an orderly market and avoid liquidity leakages due to incoherencies in the different timeframes)
  Long term: provide the right investments incentives in terms of generation, consumption and capacity
  Ensure that the maximum of capacity is allocated in the most efficient and least costly manner, while guaranteeing a certain level of security of supply
  Ensure compatibility with the general IDXB solution based on a continuous implicit allocation scheme in terms of e.g. performance
  Ensure the operational feasibility of the implementation, and the proportional cost of the mechanism with regards to the economic benefits expected
1. Introduction
1. a Objectives

## Slide 5
Aggressor
  In continuous market under paid-as-bid scheme, the participant who performed the last action on the platform which triggered a deal is called the aggressor
Economic surplus (in terms of welfare)
  In continuous market under paid-as-bid scheme, the remaining money of a deal after all matched orders are paid the price of the bids is called the surplus.
  The surplus - which is by construction non-negative (otherwise there is no deal) - is allocated to the aggressor
Intraday network congestion problem
  Situation where there is more demand for transmission capacity than available
Congestion income
  In the specific context of IDXB, the surplus generated by matching orders at their bid price following an increase of the available capacity is called the congestion income. At this stage
1. Introduction
1.b Terminology

## Slide 6: 1. Introduction 1. c. Difference between “Ranking” and “Pricing”
Ranking of capacity requests based on timestamps, i.e. on a first-come-first-served basis.
  As this mechanism enables also the implicit valorization of the capacity through PXs cross-border markets – and in some cases subject to cross-border arbitrage with the OTC market –, it is today accepted as an efficient one (see Directive 714/2009, art. 2.1)
Ranking capacity requests based on willingness to pay
  this means that capacity value - explicit (explicit price for capacity) or implicit (spread of energy orders) - is a criteria for allocated capacity. Capacity will be first allocated to the highest capacity value
  This criteria can be mixed with other criteria, for example a time criteria, which is the case in continuous trading with automatic matching
Pricing
  this means that the capacity value (or congestion rent) is extracted from an allocation. This concept refers to the pricing mechanism for a trade or capacity
It is possible to allocate capacity based on willingness to pay (market-based) and not to extract a congestion rent (ex: pay-as-cleared in an auction)
It is possible to extract a congestion rent and to allocate capacity on another basis than willingness to pay (ex: pay-as-bid in a pure first-come-first-served mechanism)
Ranking and Pricing are two different features that are not necessarily associated
Notes: 6

## Slide 7: 1. Introduction 1.d Legal Background (i)
The following articles of the directive 714/2009 deal with the market-based aspect of allocation
  Article 16.1: "Network congestion problems shall be addressed with non-discriminatory market-based solutions which give efficient economic signals to the market participants and transmission system operators involved. Network congestion problems shall preferentially be solved with non-transaction based methods, i.e. methods that do not involve a selection between the contracts of individual market participants.“
  "2.1. - Congestion-management methods shall be market-based in order to facilitate efficient cross-border trade. For that purpose, capacity shall be allocated only by means of explicit (capacity) or implicit (capacity and energy) auctions. Both methods may coexist on the same interconnection. For intra-day trade continuous trading may be used."

## Slide 8
The FG CACM deals with pricing of intraday transmission capacity
“The CACM Network Code(s) shall set out all necessary provisions for the implementation of the pan-European intraday target model supporting continuous implicit trading, with reliable pricing of intraday transmission capacity reflecting congestion (i.e. in case of scarce capacity). The method for pricing capacity and the allocation of congestion rents shall be subject to approval by the NRAs concerned.”
“As a transitional measure, direct explicit access to the capacity will also be allowed, subject to the approval by the relevant NRAs […] The removal of direct explicit access for each border shall be subject to consultation with market parties and then approval of the relevant NRAs.”
1. Introduction 1.d Legal Background (ii)
Following the FG CACM it is currently assumed that the removal of explicit access
and the introduction of pricing of capacity will occur at the same time.

## Slide 9
NWE regulators position:
By December 2011, NWE TSOs and power exchanges should present options for pricing intraday capacity in the case of congestion. Broad consultation on the options for intraday pricing should take place in 2012.
The European target model for intraday cross-border trade is for intraday capacity pricing reflecting congestion to be introduced by 2014.
It is not yet clear what the best approach will be to facilitate intraday capacity pricing and this will depend on a number of factors. Therefore TSOs, PXs and Regulators need to investigate the different options for intraday capacity pricing and their associated costs and benefits
  This relates also to another part of the final draft of the FG CACM (5.1): “ (…) Regulators will require a good understanding of the options and associated costs and benefits for each significant step in the implementation of the approved intraday roadmap.”
1. Introduction 1.d Legal Background (iii)
Capacity pricing must be subject to an in-depth analysis including a costs-benefits
one, to allow a good understanding of its impacts and enable regulatory decision in that respect

## Slide 10
Introduction
  Objective
  Terminology
  Ranking vs. Pricing
  Legal background
Ranking
  Allocation principles
  Implicit access (SOB)
  Summary
Pricing of Capacity
Appendix

## Slide 11: A question of efficiency: Who should get capacity if a congestion occurs and based on which criteria?
2. Ranking

## Slide 12: 2. Ranking 2. a. Allocation principles
No capacity available => no allocation
Sufficient* available capacity (i.e. no congestion) => Allocation based on pure FCFS
“New” capacity becomes available => allocation based on willingness to pay (idem at opening of ID market)
Limited* capacity available (i.e. congestion)  allocation based on willingness to pay
Market “A”
Market “B”
Available Capacity?
* compared to demand for capacity

## Slide 13: 2. Ranking 2.b Implicit access (SOB) – No capacity available
Offers / sellers:
100MW @ €30
100MW @ €31
100MW @ €32
Market “A”
Market “B”
Capacity = 0
No capacity, therefore it is not possible to match offers in A, with Bids in B.
Bids / buyers:
100MW @ €35
100MW @ €34
100MW @ €33

## Slide 14
Offers:
100MW @ €30
100MW @ €31
100MW @ €32
Market “A”
Market “B”
Capacity = 200
Bids:
100MW @ €35
100MW @ €34
100MW @ €33
New capacity becomes available (200MW), energy order matches are now possible.
2. Ranking 2.b Implicit access (SOB) – Additional capacity (i)

## Slide 15
35
34
33
32
31
30
200MW
€
MW
Energy Orders Matched:
Market A Market B
Allocation takes place in accordance with price (willingness to pay).
€30 with €35
€31 with €34
2. Ranking 2.b Implicit access (SOB) – Additional capacity (ii)

## Slide 16
No congestion | In case of congestion
Capacity Allocation
Pure FCFS
SOB
Automatic matching
OTC
Balancing
Capacity Allocation
-Ranking based on value criteria
SOB
Automatic matching
OTC
Balancing
2. Ranking 2. c. Summary

## Slide 17
Introduction
  Objective
  Terminology
  Legal background
  Ranking vs. Pricing
Ranking
  Allocation principles
  Implicit access (SOB)
  Summary
Pricing of Capacity
Appendix

## Slide 18: WILL THERE BE PRICING OF CAPACITY I.E. EXTRACTION OF A CONGESTION RENT?
3. Pricing of Capacity

## Slide 19
Ensuring efficient capacity allocation (done with ranking on the willingness to pay)
  Short term efficiency: ensures demand is served by the least cost generator (capacity allocated to trade with the highest buy-sell spread)
  Long term efficiency: incentives to invest generation in deficit areas, as well as increased incentives for network expansion
  How? Capacity must be allocated to the most economically efficient energy offers
  When capacity is scarce*, this involves that capacity is valued by the requesters (willingness to pay / adjustment of the underlying energy orders)
Therefore, under which conditions capacity pricing would be needed ?
  If capacity is a scarce good
  If it is a mean of valorization of capacity that can enhance the welfare by a more efficient allocation (better selection of the requests)
  If it follows a transparent pricing mechanism for the market participants (who will need to buy the capacity product to the TSOs)
The aim of pricing capacity in the intraday market should not be to maximize TSO's income, but to enhance the capacity allocation
3. Pricing of Capacity
  * Capacity may be a scarce good in the intraday time frame even though there is capacity left after the day-ahead allocation because a congestion may appear during an intraday session

## Slide 20
How to evaluate the added value of capacity pricing?
  Benefits in terms of capacity allocation efficiency - factor of:
    Added welfare gains
  Benefits in terms of congestion rent* - factor of:
    Expected amount of recalculated intraday capacity
    Expected number of hours of congested cases following recalculation of intraday capacity
    Expected price differences between hubs – i.e. willingness to pay for the capacity
    Vs.
  Costs - factor of:
  Expected costs for the implementation of the pricing mechanism
  Expected negative impact on the trading mechanism efficiency
3. Pricing of Capacity
  * Legitimate only if associated with higher welfare gains

## Slide 21: Thanks for your attention!

## Slide 22: Backup Potential solution to collect explicit price for explicit requests (OTC)

## Slide 23: Ranking Explicit access
Offers:
100MW @ €30
100MW @ €31
100MW @ €32
Market “A”
Market “B”
Capacity = 0
Bids:
100MW @ €35
100MW @ €34
100MW @ €33
Explicit request for 100 MW Capacity at a price of €4.
How to consider the explicit request alongside the Energy Market orders?

## Slide 24: Ranking Explicit & Implicit access – Additional capacity
35
34
33
32
31
30
€
MW
Energy order pairs can be viewed as making explicit capacity requests:
First Pair of energy orders value the capacity at (€35-€30)=€5
Second Pair of energy orders value the capacity at (€34-€31)=€3
Third Pair of energy orders value the capacity at (€33-€32)=€1
Results in 3 implicit requests for capacity:
100 MW @ €5
100 MW @ €3
100 MW @ €1

## Slide 25
Can be ranked along with the pending explicit request for Capacity: 100 MW @ €4.
i) 100 MW @ €5
ii) 100 MW @ €4
iii) 100 MW @ €3
iv) 100 MW @ €1
Capacity allocated according willingness to pay, thus available capacity (200MW) is allocated to top two ranked requests.
The 3 ‘implicit’ requests for Capacity:
i) 100 MW @ €5
ii) 100 MW @ €3
iii) 100 MW @ €1
Ranking Explicit & Implicit access